Evolution and Changes of Beagle back Bone Board
Revision	Additions(differences)
A4	Preliminary
A4A	Incorporated the capacitors to fix the noise issue on the display
A4B	Added a 100K pull down resistor between pins 1 and 4 of J1 to fix the serial port issue
A5.1	1.Added information on Power button and the battery access / points / 2.Final production released version.
A5.2	1) Updated the PCB to incorporate the modification that was being done on Rev A5A. There is NO difference at all in functionality between REV A5A and REV A5B. 2) Made the LEDs dimmer for those that could not sleep due to the brightness of the LEDs.
A5.3	1. Updated serial number locations. / 2. Corrected the feature table for 4 UARTS / 3. Corrected eMMC pin table to match other tables in the manual.
A5.4	1. Corrected revision listed in section 2. Rev A5A is the initial / production release. / 2. Added all the locations of the serial numbers / 3. Made additions to the compatibility list. / 4. Corrected Table 7 for LED GPIO pins. / 5. Fixed several typos. / 6. Added some additional information about LDOs and Step-Down converters. / 7. Added short section on HDMI.
A5.5	1. Release of the A5B version. / 2. The LEDS were dimmed by changing the resistors. / 3. The serial termination mode was incorporated into the PCB.
A5.6	1. Added information on Rev A5C / 2. Added PRU/ICSS options to tables for P8 and P9. / 3. Added section on USB Host / 4. Correct modes on Table 15. / 5. Fixed a few typos
A5.7	1. Updated assembly revision to A6. / 2. PCB change to add buffer to the reset line and ground the oscillator GND pin. / 3. Added resistor on PCB for connection of OSC_GND to board GND.
A6	1. Added changes for rev A6 that covered fixing of the link LED, JTAG Reset, and DHCP issue. / 2. Added PRU information and two additional signals for the PRU. / 3. Added write protection to EEPROM. / 4. Fixed numbering of subsections in Section 7.0 / 5.Fixed error in Table 9 pin 23Mode 1 should be MMC1_DAT4. / 6. Updated Table 7 to show the revision number in the EEPROM matches the revision of the board. / 7. Corrected various typos. / 8. Updated Battery Interface section to accurately document the LDO dropout at 200mV. / 9. Added SW Support section.
A6A	1) Added optional zero ohm resistor to tie GND_OSC1 to system ground. 2) Changed C106 to a 1uF capacitor. 3) Changed C24 to a 2.2uF capacitor.
B	1.Changed the processor to the AM3358BZCZ / 2.No changes in features or operation of the board resulted from this change.
C	1.This revision increased the eMMC from 2GB to 4GB